## Slide 1: Polaris Overview
April 27, 2022
Kevin Harms
Brian Homerding

## Slide 2: Introductions
Kevin Harms is a team lead of the Performance Engineering group within the Argonne Leadership Computing Facility (ALCF). His interests include working on high performance storage and I/O. Kevin received his Master of Science from Illinois Institute of Technology and his Bachelor of Science from Purdue University.
Kevin will be covering the hardware overview
Brian Homerding is a member of the Performance Engineering group within the Argonne Leadership Computing Facility (ALCF). His interests include high performance portability frameworks and compilers. Brian received his Master of Science from Northern Illinois University and his Bachelor of Arts from the University of Illinois Urbana-Champaign.
Brian will be covering the software overview

## Slide 3: Polaris
https://www.alcf.anl.gov/polaris
ALCF’s latest computational resource
  Provide a on-ramp to Aurora
Currently limited to ALCF staff as part of standup
Targeting 2H2022 for wider general access
Top500 November 2021

## Slide 4: Hardware

## Slide 5: Single AMD EPYC “milan” 7543P CPU Specs
Base Frequency | 2.8 GHz
Max Boost Clk | 3.7 GHz
# of Zen3 Cores | 32
# of Threads | 64
Total DDR4 Memory | 512 GB
# of Memory Channels | 8
DDR4 Memory BW | 204.8 GB/s
Total Shared L3 Cache | 256 MB
L2 Cache per Core | 512 KB
L1 Cache per Core | 32 KB
PCIe Gen 4 | 128 lanes (8 ports)
PCIe Gen4 BW | 64 GB/s
TDP | 225 W

## Slide 6: NVIDIA HGX A100 Specs
A100 PCIe
HGX A100 4-GPU
Ampere 7nm
 | A100 PCIe | HGX
FP64 | 9.7 TF | 38.8 TF
FP64 Tensor Core | 19.5 TF | 78 TF
FP32 | 19.5 TF | 78 TF
BF16 Tensor Core | 312 TF | 1.3 PF
FP16 Tensor Core | 312 TF | 1.3 PF
INT8 Tensor Core | 624 TOPS | 2496 TOPS
GPU Memory | 40 GB HBM2 | 160 GB HBM2
GPU Memory BW | 1.6 TB/s | 6.4 TB/s
Interconnect | PCIe Gen4 64 GB/s | NVLink 600 GB/s
Max TDP Power | 250W | 400W

## Slide 7: Polaris Single Node Configuration
# of AMD EPYC 7543P CPUs | 1
# of NVIDIA A100 GPUs | 4
Total HBM2 Memory | 160 GB
HBM2 Memory BW per GPU | 1.6 TB/s
Total DDR4 Memory | 512 GB
DDR4 Memory BW | 204.8 GB/s
# OF NVMe SSDs | 2
Total NVMe SSD Capacity | 3.2 TB
# of Cassini NICs | 2
Total Injection BW (w/ Cassini) | 50 GB/s
PCIe Gen4 BW | 64 GB/s
NVLink BW | 600 GB/s
Total GPU DP Tensor Core Flops | 78 TF

## Slide 8: Slingshot Interconnect
Rosetta Switch
Multiple QoS levels
Aggressive adaptive routing
Advanced congestion control
Very low average and tail latency
High performance multicast and reduction
64 ports x 200 Gbps
MPI hardware tag matching
MPI progress engine
One-sided operations
Collectives
2X injection bandwidth
Cassini NIC
Mellanox ConnectX NIC
SS-10 (100Gb)
Injection: ~14 TB/s
Bisection: ~24 TB/s
SS-11 (200Gb)
Injection: ~28 TB/s
Bisection: ~24 TB/s
Slingshot 11
Slingshot 10
HPE Cray MPI stack
Ethernet functionality
RDMA offload
Notes: Polaris has an option to upgrade the system to Slingshot-11, replacing the Mellanox NICs with Cassini NICs.

## Slide 9: Slingshot Configuration
11 Total dragonfly groups, 10 compute groups and 1 non-compute group
2 links/arc between each group
4 links/arc within each group (between switches of a group)
1 link from each NIC (100Gb with SS10, 200Gb when upgraded to SS11)
Notes: Point out we have multiple dragonfly groups, enabling evaluation of Rosetta traffic congestion management features.
Start with 100G Mellanox NICs and then upgrade to Cassini NICs which will allow testing of the advanced MPI messaging features.

## Slide 10: Polaris System Configuration
Apollo 6500 Gen10+
# of River Compute racks | 40
# of Apollo Gen10+ Chassis | 280
# of Nodes | 560
# of AMD EPYC 7543P CPUs | 560
# of NVIDIA A100 GPUs | 2240
Total GPU HBM2 Memory | 87.5TB
Total CPU DDR4 Memory | 280 TB
Total NVMe SSD Capacity | 1.75 PB
Interconnect | HPE Slingshot
# of Cassini NICs | 1120
# of Rosetta Switches | 80
Total Injection BW (w/ Cassini) | 28 TB/s
Total GPU DP Tensor Core Flops | 44 PF
Total Power | 1.8 MW

## Slide 11: Node Local Storage
Each compute node has two NVMe SSDs
  1.6 TB each / 3.2 TB total
Similar to Theta, ALCF provides no specific software for using SSDs
Each volume will be mounted as an ext4/xfs volume that is user accessible
Users access SSD via standard POSIX APIs
Data is destroyed when the job ends so any data users wish to keep must be moved to Grand or Eagle

## Slide 12: Storage
  Grand – Global/Center-wide file system providing main project storage
    100 PB @ 650 GB/s
    Accessed via Lustre LNET routers using Polaris gateway nodes
  Eagle – Community file system providing project storage that can be shared externally via Globus sharing
    100 PB @ 650 GB/s
    Accessed via Lustre LNET routers using Polaris gateway nodes
  Gateway nodes can provide >1 TB/s
  Home – shared home file system for convenience not for performance or bulk storage
Polaris will be connected to existing ALCF storage resources

## Slide 13: Software

## Slide 14: Polaris Software Overview
Provides an excellent platform for preparing application codes for Aurora
  All programming models available on Aurora can be tested
  Features HPE Cray (PE) Programming Environment
Provides excellent capabilities in simulation, data and learning using Nvidia’s existing HPC SDK
Support for HPE Cray MPI and MPICH via libfabric using Slingshot provider

## Slide 15: Filesystem
Polaris will have a shared home filesystem
The Eagle and Grand filesystems available and mounted
  /lus/grand
  /lus/eagle
Main project storage
  /lus/grand/projects
Community project storage
  /lus/eagle/projects

## Slide 16: Scheduler – PBS Professional
Primary commands
  qsub
    Request resources and start your script on the head node
    -A - Allocation
    -l - Options
  qstat
    Check on the status of requests
    -Q - List queues
    -f <jobid> - Detailed information about a job
    -x <jobid> - Information about a completed job
  qalter
    Update your requests
  qdel
    Cancel unneeded requests

## Slide 17: Scheduler – PBS Professional
Resource requests and placement
  Job wide options
    -l walltime=06:00:00
  Resource selection
    -l select=[<N>:]<chunk>[+[<N>:]<chunk> ...]
  Simple example with system selection (128 compute nodes on Polaris)
    -l select=128:system=polaris
Useful definitions
  chunk
    Set of resources allocated as a unit to a job
  vnode
    Virtual node. Abstract object representing a usable part of an execution host
  ncpus
    On Polaris this is equal to a hardware thread. Polaris has a single socket with 32 cores, each with 2 threads resulting in ncpus=64
  ngpus
    Number of GPUs. Generally will be four on Polaris. Could potentially be higher if using Multi Instance GPU (MIG) mode.

## Slide 18: Some useful commands for working with PBS
qsub2pbs (Available on Theta and Cooley)
  Translates Cobalt qsub command to PBS qsub command
  Pass it a Cobalt command line and get a pbs one
pbsnodes
  Provides information about the current state of nodes

## Slide 19: Running MPI Applications
Jobs run directly on the compute nodes. The mpiexec command runs applications using the Parallel Application Launch Service (PALS)
mpiexec
  Execute MPI applications on compute nodes using mpiexec
    -n Total number of MPI ranks
    -ppn Total number of MPI ranks per node
    --cpu-bind CPU binding for application
    --depth Number of CPUs per rank
    --env Set environment variables
    --hostfile Indicate file with hostname
    Full list of options available from the man page

## Slide 20: MPI Environment Variables
MPICH_GPU_SUPPORT_ENABLED
  Enable MPI operations with communication buffers on GPU-attached memory regions
MPICH_OFI_NIC_VERBOSE
  Print verbose information about NIC selection
MPICH_OFI_NIC_POLICY
  Selects the rank-to-NIC assignment policy (BLOCK, ROUND-ROBIN, NUMA, GPU, USER)
MPICH_OFI_NIC_MAPPING
  Specifies the rank-to-NIC mapping on each node

## Slide 21: Programming Environment
HPE Cray PE for Polaris
    HPE Cray MPI support for PGI offload to A100 for Multi-NIC and Multi-GPU support
    Full Rome and Milan support
NVIDIA HPC SDK will provide primary support for programming A100
SYCL/Data Parallel C++ provided via
  CodePlay computecpp compiler with Nvidia support
  LLVM via Intel DPC++ branch which supports offload to Nvidia GPUs as well as Intel GPUs

## Slide 22: Programming Models
  OpenMP w/o target
  OpenMP with target
OpenACC
  DPC++/SYCL
  CUDA
MPI +
  Kokkos
  Raja
Vendor Supported Programming Models
ECP Provided Programming Models
FORTRAN
C++
Cray
NVIDIA
LLVM
CodePlay
AMD
  HIP
C
Notes: HIP available via CUDA runtime
Kokkos and RAJA can use CUDA, OpenMP, HIP or possibly SYCL backends

## Slide 23: Python
The HPE Cray PE provides python with several builtin modules
  numpy
  scipy
  pandas
  mpi4py
Optimized data learning and analytics frameworks are available and optimized for NVIDIA libraries

## Slide 24: Data Analytics And Learning
Deep Learning
  Tensorflow and PyTorch are optimized with CuDNN.
    Other DL frameworks available and optimized by NVIDIA libraries.
  Distributed data-parallel deep learning, using libraries such as Horovod, optimized to leverage the NCCL communication library from NVIDIA
Data Analytics
  NVIDIA Rapids library for datascience and analytics
  Python environment, and Numba for GPU using the CUDA backend
Cray/HPE AI Stack
  Hyper-parameter optimization (HPO) library
  Jupyter notebooks
  SmartSim library for in-situ coupling of simulations with analytics and learning
Spark BigData Stack with modules optimized for GPU
Container environment based on singularity

## Slide 25: Additional Software
The HPE Cray PE provides several programming environments.
HPE provides compiler wrappers by default which includes various libraries (including MPI libraries)
  cc -> nvc
  CC -> nvc++
  ftn -> nvfortran
Addition software on the system is available through modules. The software available on the system is growing.
  module avail
    See what modules are currently available
  module load ...
Users can utilize Spack to install needed software directly.
  https://spack.readthedocs.io/en/latest/getting_started.html

## Slide 26: Debuggers & Profilers
Debuggers
  STAT (Stack Trace Analysis Tool)
    Stack tracing at scale
  gdb4hpc
    Parallelized gdb for HPC
  CUDA-GDB
    NVIDIA tool for debugging CUDA
  gdb
Profilers
  PAT (Performance Analysis Tool)
    Whole program performance analysis
  NVIDIA® Nsight™
    System-wide performance analysis tool

## Slide 27: Information and Help
User documentation will be added to the ALCF support center
  https://www.alcf.anl.gov/support-center
Additional information about Polaris
  https://www.alcf.anl.gov/polaris
Getting help for ALCF resources
  support@alcf.anl.gov